## Slide 1: Introduction to CUDA
Alper Kinaci, Sr. Computational Specialist
Yeguang Xue, Graduate Assistant
Research Computing Services
https://github.com/nuitrcs/intro-cuda-workshop

## Slide 2: OUTLINE
Introduction to CUDA and GPU
GPU and CPU Comparison
CUDA Programming Essentials
  Kernels
  Block & Thread Hierarchy
  Memory Hierarchy, Global and Shared Memory
  Unified Memory Model
  Atomic Operations

## Slide 3: GPU & CUDA
CUDA is a parallel computing platform and application programming interface (API)
Developed for graphics processing units (GPUs) created by Nvidia.

## Slide 4: GPU & CUDA
C (natively)
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html
C++ (natively)
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html
Fortran (PGI CUDA Fortran)
https://www.pgroup.com/resources/cudafortran.htm
Python (Numba)
http://numba.pydata.org/
Java (JCuda)
http://www.jcuda.org/
Support for Programming Languages

## Slide 5: Brief History of GPU
1975
1995
2000
2006
Early 3D consumer graphics
3Dfx Voodoo graphics
NVIDIA vs ATI Era, beginning of programmable GPUs
Modern GPU (General purpose GPU), CUDA -
Compute Unified Device Architecture

## Slide 6: Comparison of CPU and GPU
CPU
Complex compute units.
Limited cores, but each core runs fast.
High power consumption limits the increase of clock speed.
GPU
Lots of simple compute units.
Running lots of threads in parallel.
More power efficient.
The CPU and its memory are called host.
The GPU and its memory are called device.

## Slide 7: Comparison of CPU and GPU
https://www.foxrenderfarm.com/share/post-id-1166
ALU = Arithmetic Logic Unit
GPU is composed of several dozens of Streaming Multiprocessors (SMs)
SMs themselves consist of many ALUs, control logic and cache
SMs run in parallel and independently.
  Advantage: Efficiency (no waiting), scalability
  Disadvantage: Simplified parallel tasks, small communication

## Slide 8: Comparison of CPU and GPU
GPU/Cuda parallelism is better suited for Single Instruction Multiple Data (SIMD)
CPU/OpenMP is better for Multiple Instruction Multiple Data (MIMD)
Complicated work-flows with a lot of branching and heterogeneous mix of algorithms, prefer CPU/OpenMP instead of GPU/Cuda.

## Slide 9
CUDA and Other Platforms
CUDA
  Introduced in 2007 with Nvidia Tesla architecture
  Currently the most popular platform for GPU computing
OpenCL
  CUDA only runs on Nvidia GPUs
  OpenCL runs on CPUs and GPUs from many vendors
  Potential convergence with Vulkan (3D graphics and compute API like OpenGL) in the future
ROCm
  Computing platform for AMD GPUs

## Slide 10
CUDA Program Diagram
CPU
(Host)
GPU
(Device)
Memory
Memory
GPU computing requires explicit programming model
CUDA allows a single program both for host and device
Host controls the data transfer between host memory and device memory, and launches kernels on device
CPU code
GPU code
CUDA Program
PCIe

## Slide 11
CPU allocates storage on GPU
CPU copies input data from CPU to GPU
CPU launches kernels on GPU
CPU copies results from GPU to CPU
Communication (copying data) is expensive. Successful CUDA application has high ratio of computation to communication.
cudaMalloc
cudaMemcpy
<<<…,…>>>
cudaMemcpy
CUDA Program Essentials

## Slide 12
Kernel functions run on GPUs
Define kernel function
Launching kernels
__global__ void myfunc(float *d_out, float *d_in)
myfunc <<<1,1024>>>(d_out, d_in)
Number of blocks
Number of threads per block
CUDA Program Essentials: Kernels

## Slide 13
CUDA supports natively 1D to 3D for block and thread grids
myfunc <<<dim3(bx,by,bz), dim3(tx,ty,tz)>>>(…)
threadIdx
blockDim
blockIdx
gridDim
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#thread-hierarchy
CUDA makes four pieces of information available to each thread:
Thread index
Block index
Size and shape of a thread block
Size and shape of a block grid
CUDA Program Essentials:
Threads & Blocks

## Slide 14
There is a limit to the number of threads per block
On current GPUs, a thread block can contain 1024 threads
Threads are scheduled and run synchronously in groups of 32 which are called Warps
CUDA Program Essentials:
Threads & Blocks
For a kernel call with 3D block grid of 3D thread block, the block and thread ID are calculated as:
int blockId = blockIdx.x + blockIdx.y * gridDim.x + gridDim.x * gridDim.y * blockIdx.z;
int threadId = blockId * (blockDim.x * blockDim.y * blockDim.z) + (threadIdx.z * (blockDim.x * blockDim.y)) + (threadIdx.y * blockDim.x) + threadIdx.x;

## Slide 15
cudaMalloc ( void** devPtr, size_t size )
devPtr: Pointer to allocated device memory
size: Requested allocation size in bytes
cudaMemcpy ( void* dst, const void* src,
size_t count, cudaMemcpyKind kind )
dst: Destination memory address
src: Source memory address
count: Size in bytes to copy
kind: Type of transfer
CUDA Program Essentials:
Memory Management
cudaMemcpyHostToHost, cudaMemcpyHostToDevice cudaMemcpyDeviceToHost cudaMemcpyDeviceToDevice

## Slide 16
From the terminal:
Check current GPU driver version and get an instant snapshot
nvidia-smi
Print out GPU specifications
deviceQuery
Compile single code file for C/C++ Cuda runtime API
nvcc -o code.exe code.cu
Run the binary
./code.exe
CUDA Program Essentials:
Query, Compile, Run

## Slide 17
Code Example 1: cpu_serial.cpp
Create two one dimensional vectors with 500 million elements
Add each vector element by element on 1 CPU core
Record runtime
Code Example 2: cuda_serial.cu
Create two one dimensional vectors with 500 million elements
Add each vector element by element using 1 GPU thread
Record runtime
Code Example 3: cuda_parallel.cu
Create two one dimensional vectors with 500 million elements
Add each vector element by element using many GPU threads
Record runtime
CUDA Program Essentials

## Slide 18
No explicit memory management between CPU/GPU
Unified memory allows programs to allocate data that is accessible by CPUs or GPUs.
The memory migration between CPU and GPU is managed by CUDA.
CUDA Program Essentials:
Unified Memory
https://devblogs.nvidia.com/unified-memory-cuda-beginners/

## Slide 19
cudaMalloc
cudaMemcpy
Simpler and shorter codes
CPU memory allocation
GPU memory allocation
Memory migration
malloc
Memory allocation
cudaMallocManaged
CUDA Program Essentials:
Unified Memory

## Slide 20
Code Example 4: cuda_parallel_unimem.cu
Create two one dimensional vectors with 50 million elements
Use unified memory for data migration
Add each vector element by element with many GPU threads
Record runtime
CUDA Program Essentials:
Unified Memory
cudaMallocManaged (void** devPtr, size_t size,
unsigned int flags = cudaMemAttachGlobal)
devPtr: Pointer to allocated device memory
size: Requested allocation size in bytes
flags: either cudaMemAttachGlobal (default) or cudaMemAttachHost

## Slide 21
Local memory (per thread)
Share memory (per block)
Global memory
Host memory
Fast
Slow
Thread can access each other’s results using shared or global memory.
Synchronization is needed to avoid conflict between read and write operations.
CUDA Program Essentials:
Memory Hierarchy

## Slide 22
Reproduced from https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#thread-hierarchy
Thread (1,0)
Thread (0,0)
Thread (0,1)
Thread (1,0)
Thread (1,1)
Thread (2,0)
Thread (2,1)
Thread (1,1)
Thread (1,2)
Thread Block
Thread (0,0)
Thread (0,1)
Thread (0,2)
Thread
Grid 0
(Kernel 0)
Grid 1
(Kernel 1)
Per-thread local memory
Per-block shared memory
Global memory
GPU Memory

## Slide 23
CUDA Program Essentials:
Synchronization
Acts as a barrier at which all threads in the block must wait before any is allowed to proceed
Call this function to create synchronization points within the kernel
__syncthreads()
cudaDeviceSynchronize()
Blocks until the device has completed all preceding requested tasks.
Call from the host

## Slide 24
Code Example 5: shared_memory.cu
Create one dimensional array with 1024 elements
Sum every element <= ith for all i where i is the array index
Change the value in ith element with the sum
Summation for each index position should be done by a GPU thread
CUDA Program Essentials:
Shared Memory & Synchronization
__shared__
Modifier to assign a variable to shared memory
0
1
3
2
4
……………………..
1024
Thread 2
Thread 4
+
+
3
10

## Slide 25
CUDA Program Essentials:
Atomic Operations
No other threads can perform read-modify-write operations on memory (global or shared) until the current thread’s operation is complete
Often used to prevent race conditions common encountered in multi-threaded applications.
atomicAdd(), atomicSub(), atomicExch(), atomicMin(), …
atomic operation
parallel operation
parallel operation
parallel operation
atomic operation
wait for A
Thread A
Thread B
Time

## Slide 26
Code Example 6: atomics.cu
Use 1 million GPU threads to increment the components of a 16-element array
Initially, all array elements are zero
Each thread adds 1 to only one element of the array
Each element of the array is incremented by equal number of threads
CUDA Program Essentials:
Atomic Operations
int atomicAdd(int* address, int val)
Adds val to the variable value at the address

## Slide 27
Summary
GPU architecture and differences with CPU
CUDA integration with GPU
Fundamentals of CUDA programming including
  Kernels
  Blocks & Threads
  Memory management
  Global and shared memory
  Unified memory
  Atomic operations

## Slide 28: Questions?
email: quest-help@northwestern.edu
Research Computing Services